## Slide 1: 8086 Microprocessor Instruction Set
By
Mohammad Rejwan Uddin
Lecture 6
rejwan.azad@gmail.com

## Slide 2: 8086 instruction set consists of the following instructions:
Data moving instructions.
Arithmetic instructions.
Logic instructions.
String manipulation instructions.
Control transfer instructions.
Input/Output instructions.
Other instructions.

## Slide 3: Data moving instructions.
Instruction to transfer a word
MOV AX, [BP]10H ; Used to copy the byte or word from the provided source to the provided destination.
PUSH AX ; Used to put a word at the top of the stack. Used to put all the registers into the stack.
POP DX ; Used to get a word from the top of the stack to the provided location.
XCHG AX, [BX]20; Used to exchange the data from two locations.
XLAT ; translate a byte from one code to another code using a lookup table. Such as ASCII to EBCDIC. Table address in memory is found in [BX]+[AL], destination is AL by default.
Instructions to transfer the address
LEA DX, 200H ; Used to load the address of operand into the provided register.
LDS DI, [BX]30H ; Used to load DS register and other provided register from the memory
LES SI, [DI]40H ; Used to load ES register and other provided register from the memory.
Instructions for input and output port transfer
IN AL, 01H ; Used to read a byte or word from the provided port to the accumulator.
IN AL, DX ;
OUT DX, AL ; Used to send out a byte or word from the accumulator to the provided port.
Data moving instructions does not alter flags

## Slide 4: Write instructions to send 100 bytes starting from 2000:0000H to output port 00H
  MOV AX, 2000H; instructions to load segment base in DS
  MOV DS, AX
  MOV BX, 0000H; load offset of first byte
  MOV CX, 64H ; the length of string in CX
L1: MOV AL. [BX] ; get the byte into AL
OUT 00H, AL ; send to output port
INC BX ; point to next byte
LOOP L1 ; repeat until all bytes are sent

## Slide 5: Arithmetic instructions: Changes the conditional flags
Instructions to perform addition
ADD AX, [BX]10h ; Used to add the provided byte to byte/word to word.
ADC ; Used to add with carry.
AAA ; Used to adjust ASCII after addition.
DAA ; Used to adjust the decimal after the addition/subtraction operation.
Instructions to perform subtraction
SUB ; Used to subtract the byte from byte/word from word.
SBB ; Used to perform subtraction with borrow.
AAS ; Used to adjust ASCII codes after subtraction.
DAS ; Used to adjust decimal after subtraction.
INC ; Used to increment the provided byte/word by 1.
DEC ; Used to decrement the provided byte/word by 1.
NEG ; Used to negate each bit of the provided byte/word and add 1/2’s complement.
Instruction to perform multiplication
MUL ; Used to multiply unsigned byte by byte/word by word.
IMUL ; Used to multiply signed byte by byte/word by word.
AAM ; Used to adjust ASCII codes after multiplication.
Instructions to perform division
DIV ; Used to divide the unsigned word by byte or unsigned double word by word.
IDIV ; Used to divide the signed word by byte or signed double word by word.
AAD ; Used to adjust ASCII codes after division.

## Slide 6: Write instructions to convert temperature value in Fahrenheit to Celsius using C = (F – 32)*5/9
SUB AL, 20H ; AL contains F value, (F-32) is computed
MOV CL, 05H
MUL CL ; (F-32)*5 is calculated and stored in AX
MOV CL, 09H
DIV CL ; (F-32)*5/9 is computed and stored in AL

## Slide 7: Logic instruction: Changes the conditional flags
Instructions to perform logical operation
AND ; Used for adding each bit in a byte/word with the corresponding bit in another byte/word.
OR ; Used to multiply each bit in a byte/word with the corresponding bit in another byte/word.
XOR ; Used to perform Exclusive-OR operation over each bit in a byte/word with the corresponding bit in another byte/word.
NOT ; Used to invert each bit of a byte or word.
TEST ; Used to add operands to update flags, without affecting operands.
Instructions to perform shift operations
SHL/SAL ; Used to shift bits of a byte/word towards left and put zero(S) in LSBs.
SHR ; Used to shift bits of a byte/word towards the right and put zero(S) in MSBs.
SAR ; Used to shift bits of a byte/word towards the right and copy the old MSB into the new MSB.
Instructions to perform rotate operations
ROL ; Used to rotate bits of byte/word towards the left, i.e. MSB to LSB and to Carry Flag [CF].
ROR ; Used to rotate bits of byte/word towards the right, i.e. LSB to MSB and to Carry Flag [CF].
RCR ; Used to rotate bits of byte/word towards the right, i.e. LSB to CF and CF to MSB.

## Slide 8: Write instructions to count number of logic ones in a byte
  MOV CL, 08H ; number of bits to be checked
  MOV BL, 00H ; BL to count number of ones
L1: ROL AL, 01H; AL holds the byte to be tested, the ;MSB is rotated to CF
JNC L2 ; if no carry, go to test next bit
INC BL ;If carry, increment the counter counting the ones
L2: DEC CL
JNZ L1

## Slide 9: String manipulation - load, store, move, compare and scan for byte/word.
MOVS/MOVSB/MOVSW: copies CX number of bytes/word from DS:SI to ES:DI
CMPS/CMPSB/CMPSW: Compare CX number of bytes/word from DS:SI to ES:DI
LODS/ LODSB/ LODSW: load string byte/word from DS:SI to AL/AX
STOS/ STOSB/ STOSW: store string byte/word from AL/AX to DS:SI
SCAS/ SCASB/ SCASW: Compare string byte/word in AL/AX to ES:SI

## Slide 10: Write instructions to copy a string of six bytes from memory starting from 2000:0004H to 3000:0014H
CLD
MOV AX,2000H
MOV DS, AX
MOV AX, 3000H
MOV ES, AX
MOV SI, 04H
MOV DI, 14H
MOV CX, 0006H
REP MOVSB

## Slide 11: Branch Control Instructions
conditional, unconditional, call subroutine and return from subroutine.
  JMP ; Used to jump to the provided address to proceed to the next instruction.
  JA/JNBE ; Used to jump if above/not below/equal instruction satisfies.
  JAE/JNB/JNC ; Used to jump if above/not below instruction satisfies.
  JBE/JNA ; Used to jump if below/equal/ not above instruction satisfies.
  JCXZ ; Used to jump if carry flag CF = 1
  JE/JZ ; Used to jump if equal/zero flag ZF = 1
  JG/JNLE ; Used to jump if greater/not less than/equal instruction satisfies.
  JGE/JNL ; Used to jump if greater than/equal/not less than instruction satisfies.
  JL/JNGE ; Used to jump if less than/not greater than/equal instruction satisfies.
  JLE/JNG ; Used to jump if less than/equal/if not greater than instruction satisfies.
  JNE/JNZ ; Used to jump if not equal/zero flag ZF = 0
  JNO ; Used to jump if no overflow flag OF = 0
  JNP/JPO ; Used to jump if not parity/parity odd PF = 0
  JNS ; Used to jump if not sign SF = 0
  JO ; Used to jump if overflow flag OF = 1
  JP/JPE ; Used to jump if parity/parity even PF = 1
  JS ; Used to jump if sign flag SF = 1
  CALL ; Used to call a procedure and save their return address to the stack.
  RET ; Used to return from the procedure to the main program.
TET

## Slide 12: Iteration control transfer
Iteration Control Instructions
These instructions are used to execute the given instructions for number of times.
LOOP ; Used to loop a group of instructions until the condition satisfies, i.e., CX = 0
LOOPE/LOOPZ ; Used to loop a group of instructions till it satisfies ZF = 1 & CX = 0
LOOPNE/LOOPNZ ; Used to loop a group of instructions till it satisfies ZF = 0 & CX = 0
JCXZ ; Used to jump to the provided address if CX = 0

## Slide 13: Write instructions to load a constant FFH in first 100 locations in the data segment 2000H
MOV AX, 2000H
MOV DS, AX
MOV CX,0064H
MOV BX,0000H
L1: MOV [BX],0FFH
INC BX
LOOP L1

## Slide 14: Other
setting/clearing flag bits, stack operations, software interrupts, etc.
Interrupt Instructions
These instructions are used to call the interrupt during program execution.
  INT ; Used to interrupt the program during execution and calling service specified.
  INTO ; Used to interrupt the program during execution if OF = 1
  IRET ; Used to return from interrupt service to the main program
Processor Control Instructions
These instructions are used to control the processor action by setting/resetting the flag values.
  STC ; Used to set carry flag CF to 1
  CLC ; Used to clear/reset carry flag CF to 0
  CMC ; Used to put complement at the state of carry flag CF.
  STD ; Used to set the direction flag DF to 1
  CLD ; Used to clear/reset the direction flag DF to 0
  CLI ; Used to clear the interrupt enable flag to 0, i.e., disable INTR input.